Rigging wings on N4211W (without lift pins or guides installed)

- Check that spar pins aren’t protruding out of the cockpit module and aileron linkage/hardware is out of the way

- Insert port wing lifting spar as much as possible to limit dragging of spar on fuse

- Target from starboard side tip of spar into cowbell

- Insert starboard spar pin ½ way, it helps to lift port wing from the aft tip

- Insert wood wedge to prevent spar from sliding backwards

- Insert port spar pin ½ way, again lifting a little on aft tip

- View inside and make sure spar pins aren’t protruding

- Insert starboard wing making sure to lift spar as much as possible to limit dragging spar on fuse

- Insert starboard pin, lifting on aft tip a little

- Insert wood wedge to keep spar from sliding backwards

- Insert port spar pin (pip pin), it helps to let weight of wing relax and rest on starboard spar pin, perhaps push starboard wing aft a little