## Re: Smooth transision

| from [Roger Mills] | [Permanent Link] |
| --- | --- |

| Subject: | Re: Smooth transision |
| --- | --- |
| Date: | Tue, 10 Dec 2002 10:06:39 |

Paul

If you want a good long term finish, an important tip from Neville is to

carefully sand down the wing edge of the fairing until it is maybe 1mm

proud of the wing surface then lay up a chord-wise lay up of BID 2" wide

spanning the joint on the top surface of the wing to prevent stress

cracks on the edge of the fairing arising from pressure on the wing

walkway. On top of all that I found it necessary to apply a fairly thick

layer of filler for a distance of 350mm onto the wing from the fairing

curve to provide enough material to sand down to get a smooth joint.

However each wing will be different and it depends how tightly you

managed to fit the fairing to the wing. Use a 400mm straight edge to

visualise the thickness of filler you need at the root end

Regards

Roger Mills

-----Original Message-----

From: forum-owner@xxxxxxxxxxxxxxxxx

Subject: Re:  Smooth transision

Hi!Paul.

Depends entirely on how pedantic you are! I used a 12" section of half

round rain guttering with a wooden handle fixed to the back and grit

paper stuck to the rounded side and IMHO did a good job! Not before I

fell asleep onto the wing a few times though! (But there again mine was

an MKI with the fairings provided by Graham Singleton.) Regards Bob H

G-PTAG

-----Original Message-----

From: forum-owner@xxxxxxxxxxxxxxxxx

Subject:  Smooth transision

Hi all,

I am trying to get a nice transition between the wing and the fairing at

the root on my XS wings.  I have filler tapering out 250 mm but the

transition between the wing and the fairing is still obvious to the

touch.  Am I chasing my tail here or is it possible to get this to be

fairly undetectable ?

Paul McAllister

http://europa363.versadev.com

Europa Club website is at <http://www.europaclub.org.uk>

Europa Club website is at <http://www.europaclub.org.uk>